## Slide 1
NAMS Earth Science Program Update
3/29/2019

## Slide 2
Overview of the Ames Airborne Sensor Facility (ASF)
Earth Observation System (EOS) Support Element
Airborne Science Program (ASP) Support Element
Summary of Mission Activities Under NAMS
USRA / NASA Collaboration Projects
Outline

## Slide 3: The Airborne Sensor Facility at NASA Ames Research Center
EOS / ASP Facility Sensor Systems
Development and operation of a suite of remote sensing
systems for satellite cal/val, algorithm development, and
fundamental Earth science process studies
(EMAS, MASTER, PICARD, GPS/IMUs, Digital Cameras)
ASP Real-time Sensor Network Development
SAT-Com based payload communication and control
systems, that increase the productivity of the core NASA
science aircraft
ASP Payload Engineering Support
Cross-center instrument integration support (EE, ME, IT)
EOS Optical Calibration Laboratory
NIST-traceable characterizations of airborne imaging devices
The ASF is jointly supported by the EOS Project Science Office and the Airborne Science Program
PICARD Imaging Spectrometer
Hardware development
(New EMAS Data System)
Standard Payload Interfaces
Spectral Calibration
Notes: 3

## Slide 4
Task Manager
Admin Asst.
Airborne Sensor Facility USRA/NAMS Staff
NASA Ames & Armstrong Research Centers
Sensor Engineering (6)
EMAS, MASTER, PICARD instrument support
Sr. Sensor Engineers (2)
Optical Engineer
Jr. Elect. Engineer
Sensor Technicians (2)
ASF at AFRC/Palmdale-703 (6)
Airborne Sensor Network Operations
and Instrument Support
Avionics Engineer
Sensor Network Engineer (GHOC CSA)
Data Analyst
Sensor Technicians (2)
Telemetry Systems Engineer (Global Hawk reimbursable)
Data & Mission Operations (6)
L1-1B data production, field operations, software
development & IT support
Sr. Data Analysts (2)
Data Analysts (2)
Software Engineer (Zheng)
Network Admin./CSA (Windham)
Key Interfaces
NASA ARC Task Requestor: Matt Fladeland (Code SG)
EOS Senior Project Scientist: Steve Platnick
Airborne Science Program Manager: Bruce Tagg
Contract NNA16BD14CNAMS
Tasks CLIN3D and 115 (Earth Science)
20 USRA WYE
(Co-funded by EOS-Project Science Office and the Airborne Science Program)

## Slide 5: Airborne Sensor Facility
Earth Observing System
Support Element

## Slide 6: The Enhanced MODIS Airborne Simulator and the PICARD Imaging Spectrometer
EOS/ESD facility instruments intended to:
Simulate existing satellite imager products (MODIS/VIIRS)
Validate radiances and geophysical retrievals
(emphasis on cloud and aerosol science)
Prototype future imager requirements and algorithms (e.g., PACE, ACE)
Contribute to multi-disciplinary NASA field studies
EMAS: The Enhanced MODIS Airborne Simulator - an imager with high spatial resolution and broad spectral coverage (12 bands 6.7 – 13.9mm, 3.7mm, and 25 bands 448-2400nm)
PICARD: The Push-broom Imager for Cloud and Aerosol Research and Development
A wide-FOV VNIR/SWIR imaging spectrometer (205 bands 400 – 2450nm)
EMAS
PICARD HSI
ER-2 Aircraft

## Slide 7
Standard EMAS Cloud Data Products
L-2 Cloud Products –SEAC4RS
(GSFC MODIS
Atmospheres Team)
L-1 Quick-Look Product

## Slide 8: MODIS/ASTER Airborne Simulator (MASTER)
An airborne imager with high spatial resolution and broad multi-spectral (VNIR, SWIR MWIR, LWIR) coverage, used to:
Simulate ASTER, MODIS, and HyspIRI satellite imager products
Validate radiances and land-surface geophysical retrievals
Prototype future imager requirements and algorithms (e.g., HyspIRI/SBG)
Support multi-disciplinary Earth Science process studies
Includes 50 spectral bands between 430nm and 13.1mm, with 14 MWIR bands between 3.2mm and 5.3mm, and a dual-gain 4mm band
Variable spatial resolutions from 3 – 50 meters, flying on ER-2, DC-8, P-3B, others
MASTER on DC-8
SO2 Retrievals
Kilauea, HI
(JPL)

## Slide 9
Donnells Fire 8/9/2018
R-G-B
MW/LWIR
Visible
ER-2 Flight Plan
(“Bay Area Box”)
MASTER
HyspIRI Precursor Data Sets

## Slide 10: ASF Sensor Calibration Lab A NIST-Traceable Calibration Facility for Airborne Sensors
Transfer Radiometer
Integrating Spheres
Spectral Sources
Spectral & Radiometric Characterizations from 350nm – 14mm
Annual GSFC validation and oversight by the EOS Calibration Scientist
Supports multiple NASA centers
Currently supporting:
EMAS, PICARD, MASTER
Research Scanning Polarimeter (GISS)
4/5-STAR Tracking Sun Photometers
SSFR Solar Spectral Flux Radiometers
Field Spectro-Radiometers
12” Collimator & Optical Bench
FTIR and Monochromator sources
V/SWIR Transfer Radiometer
Integrating spheres
Field-portable hemispheres
Extended—area and High-Temp BB sources

## Slide 11: Airborne Sensor Facility
Airborne Science Program Support Element

## Slide 12
Payload Instrument
Payload Instrument
Payload Instrument
Ethernet
The Airborne Science Sensor Network System
ER-2
DC-8
NASDAT Network Server
Experiment Interface Panels
Auxiliary Processor & Mass Storage
Real-time Remote Operators
NASA Mission Tools Suite
Ku-Band Sat-Com
Iridium/Inmarsat
Ground Networks
Ethernet
Ethernet
Ethernet
P-3B
Extending real-time sensor webs to NASA science aircraft
ER-2
Notes: Hardware developed under ARRA; Software partly includes AIST efforts (Don Sullivan, et al)
Offers standardized hardware and software interfaces for investigator instruments

## Slide 13
Payload Instruments
Network Server
Database & Ku Telemetry Controller
Science Data Servers
Experimenter Workstations
Web-Based Users
Master Payload Control System & PDU
Payload Control GUI (Pilot / Mission Director)
Instrument Power & Control
Ethernet
Global Hawk Ground Operations Center
AIRCRAFT
GROUND
PI Hardware
Aircraft HW
GHOC HW
Iridium (4 ch)
Iridium (2 ch)
Ku-Band Sat-Com
Flight Deck
Interface Panels (8)
Link Module
NASDAT
MPCS
EIP
AC-DC TRUs
Global Hawk APCS

## Slide 14: Misc. ASP Facility Sensor Equipment
Pressurized
Camera Cannister
Electro-Optic and Video Cameras, Precision GPS & Attitude Reference Systems
Applanix POS-AV 610/510
IceBridge DMS Cameras (P-3B)
DCS Camera in Tilt-Mount
for JPL AirSWOT (B200)

## Slide 15: Airborne Sensor Facility
Summary of Mission Activities
Under NAMS

## Slide 16
Instrument Operations (Under NAMS 2016-2018)
MASTER Missions (ER-2, DC-8) | 
Year | FY Flights
2018 | 27
2017 | 27
2016 | 12
Total | 66
EMAS Missions (ER-2) | 
Year | FY Flights
2018 | 3
2017 | 1
2016 | 28
Total | 32
DMS Missions (DC-8, P-3B) | 
Year | FY Flights
2018 | 24
2017 | 73
2016 | 56
Total | 153

## Slide 17
ASP Sensor Network (Campaigns supported)
HyspIRI (ER2 2016, 2017, 2018)
MisTIC Winds ER-2 2018)
SARP (ER2 2016, 2017, 2018)
ACEPOL (ER2 2017)
GOES-R Field Campaign (ER2 2017)
ORACLES (ER2 2016)
HAP (ER2 2016, AirMSPI)
Applanix Loaner Support
Operation IceBridge (all)
Carafe (NASDAT & Applanix, WFF Sherpa)
OMG EV-2 GLISTIN (Applanix, JSC GIII)
DopplerSCATT (Applanix, JPL)
UAVSAR (Applanix, G-III)
HALO (Applanix, Langley)
Long Island Tropospheric Ozone (Applanix, Langley)
Global Hawk Campaigns
NASA: SHOUT – (WFF, 2016) & HOPE-EPOCH (AFRC, 2017)
DoD: TM Demo – Hawaii (2017)
Airborne Sensor Network Operations and Applanix Loan Support

## Slide 18
New instrument network integrations:
AVIRIS-NG**
HyTES**
CAMAL**
PRISM**
AirHARP **
Air-LUSI**
MSFC PV Solar Cells
** denotes ESTO-funded projects
FY2018 ER-2 Instrument Integration Support

## Slide 19
USRA NAMS Collaborative Efforts

## Slide 20: USRA Funded Visiting Environmental Scientist Program (1st Hire 8/1/2018, 2nd Hire 2/1/2019)
Welcome Trust – Imperial College – UBC – USRA
NIH – Mt. Sinai Icahn School of Medicine – USRA
ECHO Consortium on Perinatal Programming of Neurodevelopment
(Phase I Awarded & Phase II Awarded)
Core Cities – London, Vancouver, Accra, Dhaka, Beijing, Teheran
35 Cities Including – Atlanta, Boston, Chicago, Los Angeles, New York, San Francisco, Washington DC
Lead analysis with machine learning/deep learning to characterize within-city variability with air pollution levels and sources, open sewers, waste sites, greenness, housing quality/poverty, road safety, …
Correlating risk factors and mitigating factors such as the effect of diet (e.g, vitamin C, anti-inflammatory fatty acids) on exposure to air pollution and chemical toxicities. Small part of a 5-Year $43M NIH Grant.
USRA PI – Dr. Meytar Sorek-Hamer
USRA PI – Dr. Meytar Sorek-Hamer
… 1.5+ WYE Funding to Date
NASA Funding

## Slide 21: Joint NASA/USRA Funded IRAD for Methane Instrument Development and Airborne Flight Testing
Initial Subcontract Fully Executed 12/11/2017
Contract Mod for NAMS Option Period Implemented
Mod for Airborne Flight Experiment – signatures imminent
FINIS Phase I Deliverables (SRR, CDR, TRR)
Prof. Charles Swenson
Center for Space Engineering
Utah State University
Laboratory testing capability for 4 ppm methane measurements as observed from space with a nadir view and 60 deg solar elevation.

## Slide 22: NASA Funded IRAD – Test Bed for CubeSat Instruments
9/11/2018
Task Mod Approved
9/28/2018
Subcontract Fully Executed
Deliverables
10/23/2018 Kickoff meeting
11/02/2018 1st Weekly Tagup
Monthly Reports
CAD Model of the 6-U
CubeSat carrier

## Slide 23: USRA Funded Enhancement to the ASF Calibration Laboratory
A NIST-traceable calibration facility managed by USRA, is designed for airborne systems, it performs spectral and radiometric measurements for instruments both at Ames and other NASA centers.
USRA-funded the purchase of a $53,000 fiber laser system (below, L) which, when interfaced to a large integrating sphere (below, C) will enable full-field characterizations of a new class of push-broom imaging devices (e.g. PICARD) as well as a variety of similar systems both in NASA, and across the remote sensing community.

## Slide 24
The Ames Airborne Sensor Facility is supported by the
NASA Earth Observing System Project Science Office at GSFC and the Airborne Science Program at NASA HQ
and is staffed by USRA.
San Francisco from a NASA U-2 at 65,000 ft